## Slide 1: Extracted Tables
Total Tables: 4

## Slide 2
Page 1 - Table 1
NO. | DESCRIPTION | MATERIAL | QTY. | REMARK
1 | SHELL | SA-240-GR.316/316L | 1 | 5t
2 | SEMI. ELLIPS HEAD 2:1 | SA-240-GR.316/316L | 2 | 5t (NON.) 4.25t (MIN.)
3 | CHANNEL BODY | SA-240-GR.316/316L | 2 | 5t
4 | LIFTING LUG | SA-36 OR EQ | 2 | 12t
5 | LIFTING LUG WEAR PAD | SA-240-GR.316/316L | 2 | 5t
6 | SUPPORT LUG | SA-36 OR EQ | 4 | 10t
7 | SUPPORT LUG BOTTOM | SA-36 OR EQ | 2 | 10t
8 | SUPPORT LUG WEAR PAD | SA-240-GR.316/316L | 2 | 5t
9 | EARTHING LUG | SA-240-GR.316/316L | 2 | 5t
10 | EXPANSION BELLOW | SA-240-GR.316/316L | 1 | 8t

## Slide 3
Page 1 - Table 2
Parameter | SHELL SIDE | TUBE SIDE | Unit
CODE & STANDARD. | ASME SECT. VIII DIV. 1 2017 ED. / TEMA CLASS B 2007 ED. |  | 
FLUID. | VAPOUR & DMSO | CHILLED WATER | 
VOLUME. | 1.02 | 0.2 | CUM.
OPERATING PRESS. | 0.1 | 5 | Bar(g)
OPERATING TEMP. | 50 | 35~40 | C°
DESIGN PRESS. | 12/F.V | 10 | Bar(g)
DESIGN TEMP. | 210 | 200 | C°
TEST PRESS. HYDRO. | 16.12 | 13.34 | Bar(g)
PNEU. | – | – | 
P.W.H.T. | – | – | 
JOINT EFFICIENCY | 0.7 | 0.7 | 
RADIOGRAPHIC EXAM. | NIL | NIL | 
CORR. ALLOWANCE. | 0 | 0 | mm.
MMT | 39.55 | 8.06 | C°
NUMBERS OF PASS | 1 | 2 | 
SURF / SHELL (EFF) | 64.3 |  | m2
INSULATION | 100 (BY OTHERS) |  | mm
WIND LOAD | 32.6 |  | m/s
EMPTY WEIGHT | 2239 |  | Kg
OPERATION WEIGHT | 2358 |  | Kg

## Slide 4
Page 1 - Table 3
NO. | DESCRIPTION | QTY. | PIPE DATA SIZE | PIPE DATA SCH/THK | PIPE DATA MATERIAL | FLANGE DATA SIZE | FLANGE DATA TYPE | FLANGE DATA RATING | FLANGE DATA MATERIAL
N8 | DRAIN | 1 | DN20 | SCH. 40s | SA-312-TP.316/316L | DN20 | WNRF | 150# | SA-182-F.316/316L
N7 | VENT | 1 | DN20 | SCH. 40s | SA-312-TP.316/316L | DN20 | WNRF | 150# | SA-182-F.316/316L
N6 | WATER OUTLET | 1 | DN20 | SCH. 40s | SA-312-TP.316/316L | DN20 | WNRF | 150# | SA-182-F.316/316L
N5 | WATER INLET | 1 | DN20 | SCH. 40s | SA-312-TP.316/316L | DN20 | WNRF | 150# | SA-182-F.316/316L
N4 | CHILLED WATER OUTLET | 1 | DN80 | SCH. 40s | SA-312-TP.316/316L | DN80 | WNRF | 150# | SA-182-F.316/316L
N3 | CHILLED WATER INLET | 1 | DN80 | SCH. 40s | SA-312-TP.316/316L | DN80 | WNRF | 150# | SA-182-F.316/316L
N2 | DMSO OUTLET | 1 | DN100 | SCH. 40s | SA-312-TP.316/316L | DN100 | WNRF | 150# | SA-182-F.316/316L
N1 | DMSO INLET | 1 | DN250 | SCH. 40s | SA-312-TP.316/316L | DN250 | WNRF | 150# | SA-182-F.316/316L

## Slide 5
Page 2 - Table 1
NO. | DESCRIPTION | MATERIAL | QTY. | REMARK
1 | TUBESHEET 1 | SA-240-GR.316/316L | 1 | 45t
2 | TUBESHEET 2 | SA-240-GR.316/316L | 1 | 45t
3 | BODY FLANGE | SA-182-F.316/316L | 3 | DN600 ASME B16.5 CLASS 150# WNRF
4 | BLIND FLANGE | SA-240-GR.316/316L | 1 | 45t
5 | HEX BOLT & NUT | SA-193-B7 & SA-194-2H | 60 | 1-1/4" x 175LG
6 | PARTITION PLATE | SA-240-GR.316/316L | 1 | 5t
7 | BAFFLE PLATE | SA-240-GR.316/316L | 12 | 5t
8 | TIE ROD | SA-479-GR.316/316L | 6 | M8 Ø10
9 | NUT | SA-194-8M | 12 | M8
10 | GASKET | CNAF | 2 | 3t
11 | GASKET | CNAF | 1 | 3t
12 | TUBE (SEAMLESS) | SA-213-TP.316/316L | 273 | Ø19.05 x 1.65t